Project Description :

__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

SECTION 1:	BUILDING LIGHTING

| DESCRIPTION | BUILDING | PROPOSAL |
| --- | --- | --- |
| 1. For FACADE | NEW / HIGH RISE | OLD / LOW RISE | HISTORIC / TRADITIONAL |  |
| Kelvin (overall on facade) | ( 4 000 | 2 700 | 3 200 |  |
| Colour Rendering Index | ( 85 | ( 85 | ( 85 |  |
| Lux (overall on facade) | ( 50 | 20 | 35 |  |
| Index of Protection | ( 54 | ( 54 | ( 54 |  |

SECTION 2:	WALKWAY LIGHTING (For external works)

|  | EXTERNAL WALKWAYS | PROPOSAL |
| --- | --- | --- |
| DESCRIPTION | Celebration Route | Heritage Link | Retail Corridor | Historical Area |  |
| Pole Type Design | Very decorative | Traditional | Modern | Traditional |  |
| Bollards Type Design | Very Decorative | Traditional | Modern | Traditional |  |
| Kelvin | > 4 000 | 3 000 | 4 000 | 3 000 |  |
| Colour Rendering Index | ( 85 | ( 85 | ( 85 | ( 85 |  |
| Lux | ( 50 | ( 30 | ( 40 | ( 20 |  |
| Uniformity | > 0.6 | > 0.5 | > 0.4 | > 0.4 |  |
| Luminance | High | Low | High | Low |  |
| Height of Poles | 3.5 m | 3.5 m | 3.5 m | 3.5 m |  |
| Spacing of Poles | 9 m | 9 m | 9 m | 9 m |  |

SECTION 3:	PARKS AND LANDSCAPING

|  | PARKS AND LANDSCAPING | PROPOSAL |
| --- | --- | --- |
| DESCRIPTION | Traditional | Modern |  |
| Poles Type Design | Traditional | Modern |  |
| Bollards Type Design | Traditional | Modern |  |
| Kelvin | 4 000 | 4 000 |  |
| Colour Rendering Index | > 85 | > 85 |  |
| Lux | > 10 | > 20 |  |
| Uniformity | > 0.2 | > 0.2 |  |
| Luminance | Low | Low |  |
| Height of Poles | 3.5 m | 3.5 m |  |
| Spacing of Poles | 9 m | 9 m |  |

Note: Please refer to Page 2 for the technical and general guidelines for lighting proposal.

Technical Guidelines

For buildings that are:-

| Modern High rise (greater than 10 storeys) | More intense Light, >100 lux White range of colour Colour temperature, 4000 K Colour rendition, >85 |
| --- | --- |
|  | Architectural Features should be considered together with the surroundings |
| Traditional Historic Low Rise | Moderate Brightness, 25 lux Warm Gold and Orange Colour temperature, 2500K Colour rendition, >85 |
|  | Roofs and architectural details should be emphasized in proportional illumination to the rest of the building and surroundings. The night lighting concept should also give legibility to the building form. |

General Guidelines

| 1 | All bare light fittings and fixtures for lighting the building should be integrated with the architecture and landscape and not obstruct building features, i.e. concealed or recessed etc. Decorative fixtures will be evaluated in relation to the architectural concept. |
| --- | --- |
| 2 | Safety aspects of ground/walkway level light fixtures should be considered. |
| 3 | Light must be free from disability glare or discomfort glare. |
| 4 | Flat surfaces should not be unevenly lit unless focus is to be placed on architectural features, entries art, etc. |
| 5 | Enough light must reach the ceilings (for example in covered walkways) to avoid gloomy conditions. |
| 6 | All fittings should be accessible for maintenance and replacement. |
| 7 | Energy efficient light sources are suggested to achieve the desired lighting effect. |

PS: 	The above guidelines and technical specifications are meant to assist the designers and are not definitive.